## Slide 1: EtherChannel

## Slide 2: EtherChannel
Port Aggregation
Port aggregation allows multiple physical ports to be bundled together to form a single logical port. The switch and STP will treat the bundled ports as a single interface, eliminating the possibility of a switching loop.
Cisco’s implementation of port aggregation is called EtherChannel. EtherChannel supports Fast, Gigabit, and 10 Gigabit Ethernet ports.

## Slide 3: EtherChannel
A maximum of 8 active ports are supported in a single EtherChannel. If the ports are operating in full duplex, the maximum theoretical bandwidth supported is as follows:
• Fast Ethernet – 1600 Mbps
• Gigabit Ethernet – 16 Gbps
• 10 Gigabit Ethernet – 160 Gbps
The maximum number of supported EtherChannels on a single switch is platform-dependent, though most support up to 64 or 128 EtherChannels.

## Slide 4: EtherChannel
EtherChannels can be formed with either access or trunk ports. EtherChannels are also supported on Layer-3 interfaces.
EtherChannel for access ports provides increased bandwidth and redundancy to a host device, such as a server. However, the host device must support a port aggregation protocol.
EtherChannel for trunk connections provides increased bandwidth and redundancy to other switches.

## Slide 5: EtherChannel
EtherChannel to become active, all ports in the bundle must be configured identically, regardless if the EtherChannel is being used with access or trunk ports. Port settings that must be identical include the following:
• Speed settings
• Duplex settings
• STP settings
• VLAN membership (for access ports)
• Native VLAN (for trunk ports)
• Allowed VLANs (for trunk ports)
• Trunking encapsulation protocol (for trunk ports)

## Slide 6: EtherChannel – Manual Configuration
There are two methods of configuring an EtherChannel:
• Manually
• Dynamically, using an aggregation protocol
To manually configure two ports to join an EtherChannel:
Switch(config)# interface range gi2/23 - 24 Switch(config-if)# channel-group 1 mode on
The remote switch must also have the EtherChannel manually configured as on. Remember that speed, duplex, VLAN, and STP configuration must be configured identically across all participating ports on both switches.

## Slide 7: EtherChannel – Dynamic Configuration
Cisco switches support two dynamic aggregation protocols:
• PAgP (Port Aggregation Protocol) – Cisco proprietary aggregating protocol.
• LACP (Link Aggregation Control Protocol) – IEEE standardized aggregation protocol, originally defined in 802.3ad.

## Slide 8: EtherChannel – Dynamic Configuration
Both PAgP and LACP exchange negotiation packets to form the EtherChannel. When an EtherChannel is configured manually, no negotiation packets are exchanged.
Thus, an EtherChannel will never form if one switch manually configured the EtherChannel, and the other switch is using a dynamic aggregation protocol.
PAgP and LACP are not compatible – both sides of an EtherChannel must use the same aggregation protocol.

## Slide 9: EthernChannel - PAgP
PAgP is a Cisco-proprietary aggregation protocol, and supports two modes:
• Desirable – actively attempts to form a channel
• Auto – waits for the remote switch to initiate the channel
A PAgP channel will form in the following configurations:
• desirable desirable
• desirable auto
A channel will not form if both sides are set to auto. Also, PAgP will not form a channel if the remote side is running LACP, or manually configured.

## Slide 10: EthernChannel - PAgP
To create an EtherChannel using PAgP negotiation:
Switch(config)# interface range gi2/23 – 24 Switch(config-if)# channel-protocol pagp Switch(config-if)# channel-group 1 mode desirable
Switch(config-if)# channel-group 1 mode auto

## Slide 11: EtherChannel - LACP
LACP is an IEEE standard aggregation protocol, and supports two modes:
• Active – actively attempts to form a channel
• Passive – waits for the remote switch to initiate the channel
An LACP channel will form in the following configurations:
• active active
• active passive
A channel will not form if both sides are set to passive. Also, LACP will not form a channel if the remote side is running PAgP, or manually configured.

## Slide 12: EtherChannel - LACP
To create an EtherChannel using LACP negotiation:
Switch(config)# interface range gi2/23 – 24 Switch(config-if)# channel-protocol lacp Switch(config-if)# channel-group 1 mode active Switch(config-if)# channel-group 1 mode passive

## Slide 13: Troubleshooting EtherChannel
To view status information on all configured EtherChannels:
Switch# show etherchannel summary